## Slide 1
Bitmap
Display Window
1 to 65535 pixels
1 to 65535 pixels
1 to 4095
1 to 4095
Bitmap may be up to 65k pixels in both x and y directions
The controller displays part of the bitmap in a window which may be defined to be up to 4095x4095
Actual limits of what is displayed depends on the display resolution set by the sync generator
rtfBitmapController5 – Sizing

## Slide 2
Bitmap
Display Window
-13
-103
Sync position
The display window may be set outside of the bitmap’s area in order to account for the position relative to vertical and horizontal sync signals.
A small negative value is typically required for the window top left position in order to get the bitmap to display onscreen.
rtfBitmapController5 – Window Positioning

## Slide 3
Bitmap
Display Window
- If the display window is set outside the bounds of the bitmap, the missing data will be displayed in an out-of-bounds color (default dark red).
rtfBitmapController5 – Out-of-Bounds Coloring